## Slide 1: Ultra-low-power, Energy-minimal Computer Architectures Thesis Defense
Graham Gobieski
Advisors: Brandon Lucia, Nathan Beckmann
Committee: Brandon Lucia, Nathan Beckmann, Kenneth Mai, Todd Mowry, Tony Nowatzki
Carnegie Mellon University
Notes: Highlight publications and first authorships more

## Slide 2: ULP sensor devices enables new applications
Medical devices
Tiny satellites
Wildlife monitoring
Civil infrastructure
monitoring
Devices will number in trillions1
1Arm “How to build a trillion connected things”

## Slide 3: Typical device deployed today
Sensor
Microcontroller
(MCU)
Radio
Power source
Camaroptera
Nardello et al. Ensys 2019
10s of mW
“Ultra”-low-power is <1mW
Typical deployed device today
1
2
3
4
Notes: Order of magnitude or more lower

## Slide 4: Energy-efficiency is key
Battery lifetime determines device lifetime
Energy-harvesting device: energy determines application feasibility
Capacitor
Solar cell
Dead
Energy
stored
Time
Time ∝ Energy
Computing
Recharging
Notes: Energy determines application feasibility because most time is spent recharging, not computing. So time is proportional to energy, making some applications viable and others not.

## Slide 5: Sensor devices are severely resource constrained
Simple single-issue, in-order scalar pipelines
Memory (<256KB)
Power (<1mW)
Mobile SoC
ULP Sensor
Device
Memory
1KB
1MB
1GB
1TB
8GB DRAM + 512GB Flash
100s KB
Mobile SoC
ULP Sensor
Device
Power
1μW
1mW
1W
2-10W
100s μW
(log scale)
(log scale)

## Slide 6: Offloading is NOT viable
Communication* uses order-of-magnitude too much energy
Potential privacy concerns
Energy
Local
Compute
Offload
~20x more expensive
*over long (1+km) distances
 On-device computation matters!

## Slide 7: But existing devices are inefficient
Control/Communication
Instruction energy* breakdown:
Useful compute
(10%)
>90%
*Horowitz ISSCC 2014 + measured values
Goal: increase energy-efficiency

## Slide 8: Efficiency without sacrificing programmability
Specialization would energy-efficiency, but…
  High upfront engineering cost
  Sacrifice programmability
Applications only starting to emerge
Goal: maintain programmability
Tracking species
Infrastructure
monitoring
Chip-scale
Satellites
...
Notes: But applications for ULP sensor devices are only starting to emerge and are varied.
This makes specialization premature.
So our second goal is to maintain a high-degree of programmability while achieving high energy-efficiency.
In fact, as I’ll argue later that, programmability and efficiency are not necessary at odds; similar energy-efficiency is achievable without fixed-function specialization.

## Slide 9: Efficiency without sacrificing programmability
Specialization would energy-efficiency, but…
  High upfront engineering cost
  Sacrifice programmability
Applications only starting to emerge
Goal: maintain programmability
Tracking species
Infrastructure
monitoring
Chip-scale
Satellites
...
Not necessarily a trade-off between efficiency & programmability
Notes: But applications for ULP sensor devices are only starting to emerge and are varied.
This makes specialization premature.
So our second goal is to maintain a high-degree of programmability while achieving high energy-efficiency.
In fact, as I’ll argue later that, programmability and efficiency are not necessary at odds; similar energy-efficiency is achievable without fixed-function specialization.

## Slide 10: Need a new system stack
High energy-efficiency can be achieved across the system stack from software to silicon without compromising on programmability by leveraging new execution models to reduce instruction fetch/decode, pipeline-control and data supply energies.
Thesis
Application
Compiler
OS
Computer architecture
Silicon
Topic for another thesis
MANIC
SNAFU &
RipTide
SONIC
MANIC-Silicon
System stack
RipTide
for i in b:
a += i & 1
Notes: Why no OS? There isn’t one. Why need an OS – virtual memory.
SNAFU – coarse-grain reconfigurable array

## Slide 11: Talk outline
1Gobieski et al. Intelligence Beyond the Edge: Inference on Intermittent Embedded Systems. SysML’18, ASPLOS’19
2Gobieski et al. MANIC: A Vector-Dataflow Architecture for Ultra-Low-Power Embedded Systems. MICRO’19
3Gobieski et al. SNAFU: An Ultra-Low-Power, Energy-Minimal CGRA-Generation Framework and Architecture. ISCA’21
4Submitted to MICRO 2022
SNAFU: ULP CGRA Generation framework + arch3
3.
MANIC: ULP vector-dataflow co-processor2
2.
RipTide: Dataflow Compiler & ULP CGRA4
4.
Deploying DNNs on intermittent devices1
1.
T
C
>
+

## Slide 12: Talk outline
1Gobieski et al. Intelligence Beyond the Edge: Inference on Intermittent Embedded Systems. SysML’18, ASPLOS’19
2Gobieski et al. MANIC: A Vector-Dataflow Architecture for Ultra-Low-Power Embedded Systems. MICRO’19
3Gobieski et al. SNAFU: An Ultra-Low-Power, Energy-Minimal CGRA-Generation Framework and Architecture. ISCA’21
4Submitted to MICRO 2022
SNAFU: ULP CGRA Generation framework + arch3
3.
MANIC: ULP vector-dataflow co-processor2
2.
RipTide: Dataflow Compiler & ULP CGRA4
4.
Deploying DNNs on intermittent devices1
1.
The case for on-device inference
GENESIS & SONIC make inference viable
Why new architectures are necessary

## Slide 13: Goal: detect & transmit rare events on intermittent, harvested energy
Use DNN as filter
Events are rare
Frequency
Cloud
System
+
-
Notes: Our experience in getting DNN to run on intermittent, energy-harvesting device
What challenges would there be and what would go wrong.

## Slide 14: Why do we need local inference?
Notes: But I really want to drive this point home with some number from an analytic model we developed as part of this project.

## Slide 15: Trade-off between accuracy & energy
Accuracy
Energy
What harvester collects
What app needs

## Slide 16: GENESIS finds the optimal network
Balance energy-accuracy: maximize interesting messages sent/joule (IMpJ) harvested
Measure of overall application performance
Selected
Original
Parameter | Meaning
 | Probability of interesting event
 | True positive rate
 | True negative rate
 | Energy of sensing
 | Energy of inference
 | Energy of communication
Parameter | Meaning
 | Probability of interesting event
 | True positive rate
 | True negative rate
 | Energy of sensing
 | Energy of inference
 | Energy of communication
Notes: IMpJ takes energy cost of inference and accyracy. And it assumes we have some pre-existing knowledge of how common an event is, in this 5%.
Genesis selects not necessarily the most accurate network because it may use too much energy and reduce IMpJ
Answer:
1. Why was that point considered the original? Unmodified, uncompressed network config
2. Why is the “original” point so horrible? Uncompressed, dense
3. What is the correlation between energy and the y axis? Too much energy = lower IMPJ, too little energy = less accuracy = lower IMPJ
4. Why might the pareto optimal point not have the highest accuracy? Because the most accurate network might burn too much energy/not fit on device.

## Slide 17: Calculating IMpJ
Parameter | Meaning
 | Probability of interesting event
 | True positive rate
 | True negative rate
 | Energy of sensing
 | Energy of inference
 | Energy of communication
Parameter | Meaning
 | Probability of interesting event
 | True positive rate
 | True negative rate
 | Energy of sensing
 | Energy of inference
 | Energy of communication
Interesting messages sent/Joule harvested

## Slide 18: Other challenge: intermittent execution
Maintain correctness/progress under frequent power failures
Capacitor
Charge
Application
Progress
Full
App finished
Memory corruption
Loss of progress
 Solution: SONIC & TAILS runtime systems
  Insight: use regularity of NN inference to cheaply & frequently checkpoint progress

## Slide 19: Solution: SONIC
Solves challenge 3: correctness/progress
Insight: use regular structure of NNs to protect control, not data
for invm in range(i, 16):
for jnvm in range(j, 16):
Z[i][j] = A[i] * B[j] + P[i][j]
No need to checkpoint
Always read & write to different locations
Checkpoint loop indices
Small amount of state
NVM
Notes: Slow down & spend more time here

## Slide 20: Evaluation
RF Energy Harvester
Measurement MCU
Relay
MCU (under test)
Programmer
Built SONIC & TAILS: intermittence-safe inference runtimes
First DNN on intermittent, energy-harvesting system
7x reduction in energy v. prior state-of-the art

## Slide 21: Why new architectures?
Process technology
Gaps in support: e.g. no on-chip multiplier, no vector left-shift
No caches
*Horowitz ISSCC 2014 + measured values
Fetch/Decode (40-50%)
Register file (20%)
Other control
Instruction energy* breakdown:
But something fundamentally wrong,
Useful compute
(10%)
ASICs would improve this, but trade programmability/flexibility

## Slide 22: Fundamental trade-offs
High
Performance
Low Power
High
Programmability
Not as well studied
Well-studied
(GPUs, OOO, SIMD)
Well-studied (ASICs)
Notes: Green portion – not as well explored.

## Slide 23: Fundamental trade-offs
High
Performance
Low Power
High
Programmability
Not as well studied
Manic
x
SNAFU
x
Well-studied
(GPUs, OOO, SIMD)
Well-studied (ASICs)
RipTide
x
Notes: Green portion – not as well explored.

## Slide 24: Talk outline
1Gobieski et al. Intelligence Beyond the Edge: Inference on Intermittent Embedded Systems. SysML’18, ASPLOS’19
2Gobieski et al. MANIC: A Vector-Dataflow Architecture for Ultra-Low-Power Embedded Systems. MICRO’19
3Gobieski et al. SNAFU: An Ultra-Low-Power, Energy-Minimal CGRA-Generation Framework and Architecture. ISCA’21
4Submitted to MICRO 2022
SNAFU: ULP CGRA Generation framework + arch3
3.
MANIC: ULP vector-dataflow co-processor2
2.
RipTide: Dataflow Compiler & ULP CGRA4
4.
Deploying DNNs on intermittent devices1
1.
The case for on-device inference
GENESIS & SONIC make inference viable
Why new architectures are necessary

## Slide 25: Talk outline
1Gobieski et al. Intelligence Beyond the Edge: Inference on Intermittent Embedded Systems. SysML’18, ASPLOS’19
2Gobieski et al. MANIC: A Vector-Dataflow Architecture for Ultra-Low-Power Embedded Systems. MICRO’19
3Gobieski et al. SNAFU: An Ultra-Low-Power, Energy-Minimal CGRA-Generation Framework and Architecture. ISCA’21
4Submitted to MICRO 2022
SNAFU: ULP CGRA Generation framework + arch3
3.
MANIC: ULP vector-dataflow co-processor2
2.
RipTide: Dataflow Compiler & ULP CGRA4
4.
Deploying DNNs on intermittent devices1
1.
Vector-dataflow execution
MANIC Silicon

## Slide 26: MANIC: ULP Vector-dataflow processor
Reduce instruction supply energy + VRF energy
Maintain high-degree of programmability to support future kernels
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Notes: Mention ELM as related work here.

## Slide 27: Scalar execution model
for i in 0...3:
load r0, &a[i]
mul r1, r0, r0
add r2, r1, r0
store &b[i], r2
load
mul
add
store
Dataflow
mul
register
add
register
store
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
register
load
register
Related: MSP430, ARM M0
Dataflow
Control-flow

## Slide 28: Scalar execution model
for i in 0...3:
load r0, &a[i]
mul r1, r0, r0
add r2, r1, r0
store &b[i], r2
load
mul
add
store
Dataflow
add
register
store
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
register
load
register
mul
register
Dataflow
Control-flow

## Slide 29: Scalar execution model
for i in 0...3:
load r0, &a[i]
mul r1, r0, r0
add r2, r1, r0
store &b[i], r2
load
mul
add
store
Dataflow
store
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
register
load
register
mul
register
register
add
Dataflow
Control-flow

## Slide 30: Scalar execution model
for i in 0...3:
load r0, &a[i]
mul r1, r0, r0
add r2, r1, r0
store &b[i], r2
load
mul
add
store
Dataflow
register
load
register
mul
register
add
register
store
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Repeat fetches + decodes
Read and write to RF
Example Program
Dataflow
Control-flow

## Slide 31: Scalar execution is inefficient
Memory
Compute + Control
ICache access
DCache access
Energy wasted on instruction & data supply

## Slide 32: Vector execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
vload:
vmul:
vadd:
vstore:
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
Vector Register
Dataflow
Control-flow

## Slide 33: Vector execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
vload:
vmul:
vadd:
vstore:
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
Vector Register
Dataflow
Control-flow

## Slide 34: Vector execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
vload:
vmul:
vadd:
vstore:
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
Vector Register
Dataflow
Control-flow

## Slide 35: Vector execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
vload:
vmul:
vadd:
vstore:
Read and write to VRF
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
Vector Register
v[1]
v[0]
v[2]
Dataflow
Control-flow

## Slide 36: Vector execution loses on VRF accesses
Memory
Compute + Control
ICache access
DCache access
Vector
Memory
Compute + Control
ICache
DCache access
Vector register file
Notes: Size of VRF > scalar RF  accessing VRF > scalar RF

## Slide 37: MANIC’s Vector-dataflow execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[0]
v[0]
v[1]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
Dataflow
Control-flow
Notes: First we buffer a window of instructions
Then we analyze the dataflow between instruction
And then we execute a single element across multiple instructions before moving onto the next element and so on.

## Slide 38: MANIC’s Vector-dataflow execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[0]
v[1]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
v[0]
Dataflow
Control-flow

## Slide 39: MANIC’s Vector-dataflow execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[0]
v[1]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
v[0]
Dataflow
Control-flow

## Slide 40: MANIC’s Vector-dataflow execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[1]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
v[0]
v[0]
Dataflow
Control-flow

## Slide 41: MANIC’s Vector-dataflow execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
v[0]
v[0]
v[1]
Dataflow
Control-flow

## Slide 42: MANIC’s Vector-dataflow execution
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &b, v2
vload
vmul
vadd
vstore
Dataflow
Energy |  |  | 
Model | Insns | RF Reads | RF Writes
Scalar |  |  | 
Vector |  |  | 
Vector-Dataflow |  |  | 
Example Program
Vector Register
Vector Register
vload:
vmul:
vadd:
vstore:
v[0]
v[0]
v[0]
v[0]
v[1]
v[1]
v[1]
v[1]
v[2]
v[2]
v[2]
v[2]
Dataflow
Forwarding
Dataflow
Control-flow

## Slide 43: Kill annotations eliminate VRF writes
Example Program:
vload v0, &a
vmul v1, v0, v0
vadd v2, v1, v0
vstore &c, v2
Vector Register
Vector Register
Vector Register
…
vadd v3, v1, v2
VRF
Lots of VRF writes!
But the compiler knows:
vload v0, &a
vmul v1, v0, v0
vadd v2, v1.k, v0.k
vstore &c, v2.k
Annotate when registers are finally consumed (dead)
Hardware doesn’t write dead values
Vector Register
Vector Register
Vector Register
Vector Register
VRF
No writes
Notes: Hardware needs to support the worst case – the possibility of a later instruction using v1 and v2.

## Slide 44: MANIC reduces energy without costing programmability
Memory
Compute + Control
ICache access
DCache access
Vector
Memory
Compute + Control
ICache
DCache access
Vector register file
Dataflow
Memory
Compute + Control
ICache
DCache access
Vector register file
Vector-dataflow execution
  Vector execution reduces instructions fetched
  Dataflow execution eliminates VRF reads
Kill annotations: compiler hints to hardware when VRF writes can be elided
Notes: I’m going to skip the microarchitecture for the sake of time.

## Slide 45: Silicon prototype to evaluate
Goal: compare execution models in silicon
Complete standalone system
Five different designs
Intel 22nm bulk FinFet (HVT)
Embedded MRAM
Notes: Some would say is overkill, we say it was necessary and opens up future research directions.

## Slide 46: Overview of chip
Goal: compare execution models in silicon
RISC-V
Scalar Core
2KB
I$
4KB D$
I2C
4KB
VRF
Boot ROM
64KB
SRAM
256KB
MRAM
Main
Memory
MANIC
Arbiter
Arbiter
GPIO
IO Bus
Main
memory
$
Core
IO
Scalar
Main
memory
$
Core
IO
Vector
Vector
Main
memory
$
Core
IO
MANIC
Main
memory
$
Core
IO
Accel
Main
memory
$
Core
IO
Vector
VRF
MANIC
Accelerator
FFT, Sort, DConv
Vector w/
custom VRF
Top-level control
MANIC
Redo this slide

## Slide 47: Overview of chip

## Slide 48: MANIC Microarchitecture
Scalar
Core
Rename
Instruction Buffer
VDecoder
v0 | f0
v1 | f2
v2 | f1
v5 | f3
Decode & Rename
4KB
4KB
VRF
Vector index
MUX
+1
0
Insn index
MUX
+1
0
Vissue
VExecute
Data
Address
×
MUX
ALU
Mul
Execute
VMemory
4KB D$
MUX
VWriteback
MUX
MUX
Forwarding Buffer
16B
VGate
Instruction Buffer
Vissue

## Slide 49: Chip micrograph
MANIC
MRAM
SRAM
MANIC
Scalar
Caches

## Slide 50: MANIC is energy-efficient & ULP
Peak efficiency: 256MOPS/mW
  (2.6x better than prior SOTA)
ULP: 19μW @ 0.4V & 4MHz

## Slide 51: MANIC is energy-efficient & ULP
Peek efficiency: 256MOPS/mW
  (2.6x better than prior SOTA)
ULP: 19μW @ 0.4V & 4MHz
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
Vector
MANIC
65% & 12% less than scalar, vector

## Slide 52: So why is MANIC not better?
Problem: resource sharing  gate toggling  burns energy
ld
ld
x
+
st
ld
ld
x
+
st
…
…
ld
ld
x
+
st
…
ld
ld
x
+
st
…
ld
ld
x
+
st
…
VIssue
VGate
VExecute
VMemory
VWriteback
Time
Pipeline stage
MANIC Pipeline
Baseline Vector Pipeline
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
…
…
ld
ld
ld
ld
ld
…
VIssue
VExecute
VMemory/
VWriteback
Time

## Slide 53
Problem: resource sharing  gate toggling  burns energy
Address generation
0x80000000 + 0x1
0x80000001 + 0x1
…
Data compute
-5 + 6
-102 + -12
…
v.
add ptr, ptr, 1
add z, a, b
for i in 0…n:
ld a, &ptr
ld b, &ptr,
add ptr, ptr, 1
add z, a, b
st &ptr, z
Dynamic ranges are very different
Operands look very different in binary
So why is MANIC not better?

## Slide 54: Toggling of shared resources
Address generation
0x80000000 + 0x1
0x80000001 + 0x1
…
Data compute
-5 + 6
-102 + -12
…
v.
add ptr, ptr, 1
add z, a, b
Adder
Time: 0
Address generation
0x80000000
0x1
0x80000001
Adder
Time: 1
Data compute
-5
6
1
Adder
Time: 2
Address generation
0x80000001
0x1
0x80000002
A
B
Output
Internal Node
Time
Lots of toggling!
Notes: Through our experience taping out MANIC we observed that a significant amount of dynamic energy was being burned due to operations sharing pipeline resources.
Baseline design doesn’t have same problem. Mention??

## Slide 55: MANIC is energy-efficient
MANIC uses 2.8x less energy than scalar
Notes: Seven kernels – all having application in ML

## Slide 56: Talk outline
1Gobieski et al. Intelligence Beyond the Edge: Inference on Intermittent Embedded Systems. SysML’18, ASPLOS’19
2Gobieski et al. MANIC: A Vector-Dataflow Architecture for Ultra-Low-Power Embedded Systems. MICRO’19
3Gobieski et al. SNAFU: An Ultra-Low-Power, Energy-Minimal CGRA-Generation Framework and Architecture. ISCA’21
4Submitted to MICRO 2022
SNAFU: ULP CGRA Generation framework + arch3
3.
MANIC: ULP vector-dataflow co-processor2
2.
RipTide: Dataflow Compiler & ULP CGRA4
4.
Deploying DNNs on intermittent devices1
1.
Vector-dataflow execution
MANIC Silicon

## Slide 57: Talk outline
1Gobieski et al. Intelligence Beyond the Edge: Inference on Intermittent Embedded Systems. SysML’18, ASPLOS’19
2Gobieski et al. MANIC: A Vector-Dataflow Architecture for Ultra-Low-Power Embedded Systems. MICRO’19
3Gobieski et al. SNAFU: An Ultra-Low-Power, Energy-Minimal CGRA-Generation Framework and Architecture. ISCA’21
4Submitted to MICRO 2022
SNAFU: ULP CGRA Generation framework + arch3
3.
MANIC: ULP vector-dataflow co-processor2
2.
RipTide: Dataflow Compiler & ULP CGRA4
4.
Deploying DNNs on intermittent devices1
1.
What is a CGRA? What is SNAFU?
Design choices that minimize energy (reducing toggling + buffers)
SNAFU-Arch v. MANIC & ASICs

## Slide 58: CGRA Overview
Collection of processing elements (PE) connected via NoC
  PEs have heterogenous operation
  Connections/configuration dictated by compiler
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…

## Slide 59: CGRA Overview
Collection of processing elements (PE) connected via NoC
  PEs have heterogenous operation
  Connections/configuration dictated by compiler
1. vload v0, &a
2. vload v1, &b
3. vmul v2, v0, v1
4. vredsum v3, v2
5. vstore &c, v3
Vector assembly
dot_product():
Extract
1
3
4
5
2
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
1
2
3
4
5
Schedule
Notes: Spatially schedule

## Slide 60: CGRA Operation
1. vload v0, &a
2. vload v1, &b
3. vmul v2, v0, v1
4. vredsum v3, v2
5. vstore &c, v3
Vector assembly
dot_product():
1
3
4
5
2
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
1
2
3
4
5
Cycle: 1
0
0

## Slide 61: CGRA Operation
1. vload v0, &a
2. vload v1, &b
3. vmul v2, v0, v1
4. vredsum v3, v2
5. vstore &c, v3
Vector assembly
dot_product():
1
3
4
5
2
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
1
2
3
4
5
Cycle: 2
1
1
0

## Slide 62: CGRA Operation
1. vload v0, &a
2. vload v1, &b
3. vmul v2, v0, v1
4. vredsum v3, v2
5. vstore &c, v3
Vector assembly
dot_product():
1
3
4
5
2
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
1
2
3
4
5
Cycle: 3
2
2
1
0

## Slide 63: CGRA Operation
1. vload v0, &a
2. vload v1, &b
3. vmul v2, v0, v1
4. vredsum v3, v2
5. vstore &c, v3
Vector assembly
dot_product():
1
3
4
5
2
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
1
2
3
4
5
Cycle: 4
3
3
2
0
1

## Slide 64: Why a CGRA?
Coarse-grain reconfigurable array
Most
Least
Programmability/Flexibility
×
×
×
ASIC
FPGA*
Scalar
Vector
×
*FPGA is potentially more flexible than scalar/vector but is difficult to program
×
CGRA
Most
Least
Energy-efficiency
×
×
×
Scalar
ASIC
CGRA***
×
**Might be less efficient than vector for highly-vectorizable workloads
×
Vector
FPGA**
***For common set workloads including ML/DSP
Notes: Spectra
Cut?

## Slide 65: SNAFU generates ULP CGRA
Generates complete RTL for arbitrary topology ready for synthesis
Abstract CGRA topology
SNAFU-Arch
module PE
(input clk,
input data);
SystemVerilog
Description
Extendable compiler that can target generated CGRA
vload v0, &a
vaddi v1, v0, 5
vstore &b, v1
Vectorized C/C++ Code
DAG
Scheduled CGRA
ILP Solver
Can be generated from code

## Slide 66: SNAFU generates ULP CGRAs
Bring-your-own-functional-unit
Standardized interface for incorporating custom logic
Latency insensitive
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
Standard
interface
Your logic
Notes: What are the relevant related work? Copy table from paper in new slide around here. Or show motivating power graph.

## Slide 67: What makes SNAFU different?
Prior work
Notes: What are the relevant related work? Copy table from paper in new slide around here. Or show motivating power graph.

## Slide 68: Design choices that reduce energy: Spatial Vector Dataflow
Address generation
0x80000000 + 0x1
0x80000001 + 0x1
…
Data compute
-5 + 6
-102 + -12
…
Problem: resource sharing  gate toggling  burns energy
Solution: one operation/PE/kernel invocation
v.
add ptr, ptr, 1
add z, a, b
for i in 0…n:
ld a, &ptr
ld b, &ptr,
add ptr, ptr, 1
add z, a, b
st &ptr, z
Notes: Through our experience taping out MANIC we observed that a significant amount of dynamic energy was being burned due to operations sharing pipeline resources.
Baseline design doesn’t have same problem. Mention??

## Slide 69: Design choices that reduce energy: Spatial Vector Dataflow
Address generation
0x80000000 + 0x1
0x80000001 + 0x1
…
Data compute
-5 + 6
-102 + -12
…
v.
add ptr, ptr, 1
add z, a, b
Adder
Time: 0
Address generation
0x80000000
0x1
0x80000001
Adder
Time: 1
Data compute
-5
6
1
Adder
Time: 2
Address generation
0x80000001
0x1
0x80000002
A
B
Output
Internal Node
Time
Lots of toggling!
Notes: Through our experience taping out MANIC we observed that a significant amount of dynamic energy was being burned due to operations sharing pipeline resources.
Baseline design doesn’t have same problem. Mention??

## Slide 70: Design choices that reduce energy: Spatial Vector Dataflow
Adder
Time: 0
-5
6
1
Data compute
Adder
Time: 1
-102
-12
-114
Adder
Time: 2
-3
5
2
Adder
Time: 0
0x80000000
1
Adder
Time: 1
0x80000001
1
Adder
Time: 2
1
Address generation
0x80000002
0x80000001
0x80000002
0x80000003
Notes: Through our experience taping out MANIC we observed that a significant amount of dynamic energy was being burned due to operations sharing pipeline resources.
Baseline design doesn’t have same problem. Mention??

## Slide 71: Design choices that reduce energy: Spatial Vector Dataflow
Adder
Time: 0
-5
6
1
Data compute
Adder
Time: 1
-102
-12
-114
Adder
Time: 2
-3
5
2
Adder
Time: 0
0x80000000
1
Adder
Time: 1
0x80000001
1
Adder
Time: 2
1
Address generation
0x80000002
0x80000001
0x80000002
0x80000002
2 Adders, but less toggling overall  less dynamic energy
A
B
Output
Internal Node
Time
Much less toggling
Notes: Through our experience taping out MANIC we observed that a significant amount of dynamic energy was being burned due to operations sharing pipeline resources.
Baseline design doesn’t have same problem. Mention??

## Slide 72
Buffers are primary sink of energy
Buffering at producer eliminate duplication at consumers
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
Buffers @ every router
Buffers @ producer & consumer
Buffers @ producer
Why? Clock speed
Signal can travel ~11mm in 1ns1
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
C
r
B
M
r
Allows broadcast to multiple consumers w/out duplication
S
S
S
Design choices that reduce energy: Multi-hop bufferless NoC
1 HyCUBE: A CGRA with Reconfigurable Single-cycle Multi-hop Interconnect. DAC’17
Notes: Be firm on 11mm travel distance

## Slide 73: Design choices that reduce energy: Ordered dataflow1
S
r
r
r
r
B
r
r
r
r
S
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
…
1
2
3
4
5
Fires as soon as both inputs valid
No need to tag operations and make sure inputs have same tags
Compiler does not need to reason about timing
1Weng et al. A Hybrid Systolic-Dataflow Architecture for Inductive Matrix Algorithms. HPCA’26.
No re-ordering of operations allowed (memory resolves in order)
Asynchronous dataflow firing

## Slide 74: SNAFU generated SNAFU-Arch
M
= Load/store PE
S
= Scratchpad PE
B
= Basic ALU PE
C
= Multiplier PE
Main memory
Configurator
Control
stream
1KB
CGRA memory interface
SNAFU-Arch
Multi-hop,
bufferless NoC
S
r
r
r
r
B
r
r
r
r
B
r
r
r
r
B
r
r
r
r
S
r
r
r
r
B
r
r
r
r
B
r
r
r
r
B
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
B
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
B
r
r
r
r
B
r
r
r
r
C
r
r
r
r
M
r
r
r
r
S
r
r
r
r
S
r
r
r
r
S
r
r
r
r
M
r
r
r
r
S
r
r
r
r
C
r
r
r
r
B
r
r
r
r
B
r
r
r
r
C
r
r
r
r
S
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
M
r
r
r
r
1KB
1KB
1KB
1KB
1KB
1KB
1KB
Notes: Why this topology and PEs? Fit all of the benchmarks we wanted to run. Mesh is a reasonable topology for hardware synthesis/routing.

## Slide 75: How do we evaluate?
All systems implemented entirely in RTL
Sub-28nm industrial process w/ compiled memories
Energy extracted from post-synthesis annotate switching
Comparison points
RISC-V
Scalar
Benchmarks
FFT, DWT
Sort
Viterbi
DMM, DMV, DConv
SpMM, SpMV, SpConv
VRF
Vector
MANIC
SNAFU-Arch
1
2
3
4

## Slide 76: SNAFU is fast and efficient
Energy
Performance
81%
9.9x
Notes: Don’t blaze through the results! SNAFU destroys the competition!
Iso-area comparison?
Metric: Word done/input power
Varies by application requirements; some are latency sensitive than others

## Slide 77
47%
18%
33% energy improvement
Is there room for improvement?
SNAFU is ≈10x more efficient than scalar core
Offloading more  improved system energy-efficiency
Notes: We’ve previously seen these results, but they do a good job of showing the opportunity for outer-loops.
Related work: Trips, Wavescalar, Tony’s work, DAC pubs

## Slide 78: SNAFU only targets affine inner loops
void smm(int *A, ... , int rows, int cols) {
...
for(int i = 0; i < rows; i++) {
...
for(int j = j_start; j < j_end; j++) {
...
for(int k = k_start; k < k_end; k++) {
int w = clip(f * B[k], 5);
int *d = dest_ptr + Bcol[k];
*d += w;
}
}
...
}
}
Notes: We’ve previously seen these results, but they do a good job of showing the opportunity for outer-loops.
Related work: Trips, Wavescalar, Tony’s work, DAC pubs

## Slide 79: SNAFU only targets affine inner loops
void smm(int *A, ... , int rows, int cols) {
...
for(int i = 0; i < rows; i++) {
...
for(int j = j_start; j < j_end; j++) {
...
for(int k = k_start; k < k_end; k++) {
int w = clip(f * B[k], 5);
int *d = dest_ptr + Bcol[k];
*d += w;
}
}
...
}
}
vlh v0, B
vmulx v0, v0, f
vclipi v0, v0, 5
vlh v1, Bcol + k
vlxh v2, dest_ptr, v1
vadd v0, v0, v2
vsxh dest_ptr, v0, v1
Vector assembly
Low productivity
Expert-level knowledge
Notes: We’ve previously seen these results, but they do a good job of showing the opportunity for outer-loops.
Related work: Trips, Wavescalar, Tony’s work, DAC pubs

## Slide 80: Talk outline
1Gobieski et al. Intelligence Beyond the Edge: Inference on Intermittent Embedded Systems. SysML’18, ASPLOS’19
2Gobieski et al. MANIC: A Vector-Dataflow Architecture for Ultra-Low-Power Embedded Systems. MICRO’19
3Gobieski et al. SNAFU: An Ultra-Low-Power, Energy-Minimal CGRA-Generation Framework and Architecture. ISCA’21
4Submitted to MICRO 2022
SNAFU: ULP CGRA Generation framework + arch3
3.
MANIC: ULP vector-dataflow co-processor2
2.
RipTide: Dataflow Compiler & ULP CGRA4
4.
Deploying DNNs on intermittent devices1
1.
What is a CGRA? What is SNAFU?
Design choices that minimize energy (reducing toggling + buffers)
SNAFU-Arch v. MANIC & ASICs

## Slide 81: Talk outline
SNAFU: ULP CGRA Generation framework + arch
3.
MANIC: ULP vector-dataflow co-processor
2.
RipTide: Dataflow Compiler & ULP CGRA
4.
Deploying DNNs on intermittent devices
1.
T
C
>
+
What makes RipTide stand out
Control-flow-in-the-NoC
RipTide v. SNAFU & ASICs

## Slide 82: Overview of RipTide
Goal: energy-efficiency by offloading more w/out added programmer effort
T
C
>
+
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}
RipTide’s
Dataflow
Compiler
C code

## Slide 83: Overview of RipTide
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
Goal: energy-efficiency by offloading more w/out added programmer effort
T
C
>
+
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}
RipTide’s
Dataflow
Compiler
Optimized
Dataflow Graph
C code
RipTide’s ULP CGRA
R
R

## Slide 84: RipTide v. Systolic CGRAs
T
C
>
+
Examples: ULP-SRP, ISA, HyCube, 4D-CGRA, etc.
Pros: high throughput & area efficiency
Cons: limited to regular programs, mapping is hard
void test(int *a, int *b,
int *z, int n) {
while(a[i] != 0) {
for(int i = 0; i < n; i++) {
...
}
}
}
void test(int *a, int *b,
int *z, int n) {
while(a[i] != 0) {
for(int i = 0; i < n; i++) {
...
}
}
}
Riptide:
✓ Irregular loops & memory

## Slide 85: RipTide v. Alternative-dataflow CGRAs
T
C
>
+
Examples: Revel, Plasticine, SNAFU, etc.
Pros: high throughput & more flexibility v. systolic
Cons: programs must fit patterns, usually performance-oriented
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
if(a[i] < 0) {
z[i] = 0;
}
z[i] = b[i];
}
}
Store-store
dependence
Riptide:
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
if(a[i] < 0) {
z[i] = 0;
}
z[i] = b[i];
}
}
✓ Memory ordering

## Slide 86: RipTide v. Classic dataflow machines
T
C
>
+
Examples: Wavescalar, SGMF, Trips, TTDA, etc.
Pros: high throughput & general-purpose
Cons: high power & energy
✓ Energy-efficient & ultra-low-power
Watts
Classic DF
RipTide
10s W
<1mW
4 orders of magnitude

## Slide 87: RipTide’s primitives save energy
T
C
>
+
D
A
T
A
1
A
if(D) out = in
Steer gates
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
int t2 = 0;
if(a[i] < 0) {
int t1 = b[i] * 2;
t2 = t1 << a[i];
}
z[i] = t2;
}
}
a[i] = 2
Selection
int t2 = 0;
int t1 = b[i] * 2;
t2 = t1 << a[i];
a[i] < 0
Both sides fire  wastes energy

## Slide 88: RipTide’s primitives save energy
T
C
>
+
Carry gates
C
D
A
B
Init
Block
D, B;
Pop D, B
!D;
Pop D
A;
Pop A
State
machine
if(state == I) out = in
else if(D) out = in
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
...
}
}
}
C
C
Job: enforce order across iterations & nests
No tagging  saves energy
+

## Slide 89: CF-in-NoC enables sophisticated workloads
T
C
>
+
Control-flow operations numerous, but simple
Wasteful to allocate to PEs
Buffering on PEs  more energy
CF ops ≈ MUX
CF-in-NoC enables fusing
Available PEs
46% of operations are control-flow

## Slide 90: CF-in-NoC enables sophisticated workloads
Control-flow operations numerous, but simple
Routers have almost all hardware already!
Switch
Router
Switch
Switch
Router
CF-Modules
T
C
>
+
RipTide’s routers

## Slide 91: RipTide CGRA
T
C
>
+
CF
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
CF
R
R
R
R
St
R
R
R
R
A
R
R
R
R
A
R
R
R
R
St
R
R
R
R
M
R
R
R
R
M
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
CF
R
R
R
R
CF
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
A
R
R
R
R
M
R
R
R
R
M
R
R
R
R
St
R
R
R
R
A
R
R
R
R
A
R
R
R
R
St
R
R
R
R
CF
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
M
R
R
R
R
CF
R
R
R
R
RISC-V
Scalar Core
CGRA
Control
CGRA
Configurator
Memory
Memory
Memory
Memory
M
M
St
CF
A
Memory
Multiplier
Stream
Arithmetic
Control-flow
CF-modules

## Slide 92: How do we evaluate?
All systems implemented entirely in RTL
Sub-28nm industrial process w/ compiled memories
Energy extracted from post-synthesis annotate switching
Comparison points
RISC-V
Scalar
Benchmarks
FFT
Sort
BFS, DFS
DMM, DMV, DConv
SpMM, SpMV, SpConv
VRF
Vector
SNAFU
1
2
3
T
C
>
+
T
C
>
+
RipTide
4

## Slide 93: RipTide is more efficient & faster than SNAFU
T
C
>
+
Energy savings
Speedup
6.6x
6.2x

## Slide 94: RipTide is more efficient & faster than SNAFU
T
C
>
+
Energy savings
Speedup
6.6x
6.2x
Without a line of assembly!

## Slide 95: CF-in-the-NoC makes it possible
T
C
>
+

## Slide 96: How close is RipTide to ASIC designs?
And what is the cost of RipTide’s reconfigurability & programmability?
1. Fast Fourier transform (FFT)
2. Dense matrix-matrix multiply (DMM)
3. Sort

## Slide 97: Quantifying the (low) cost of programmability Three ASICs in same technology
92.5x
10.2x
19.5x

## Slide 98: Quantifying the (low) cost of programmability Three ASICs in same technology
2.9x more energy
1.9x
3.0x
3.7x

## Slide 99: Quantifying the (low) cost of programmability Three ASICs in same technology
2.3x more energy
45%
2.6x
3.0x

## Slide 100: Talk outline
SNAFU: ULP CGRA Generation framework + arch
3.
MANIC: ULP vector-dataflow co-processor
2.
RipTide: Dataflow Compiler & ULP CGRA
4.
Deploying DNNs on intermittent devices
1.
T
C
>
+
What makes RipTide stand out
Control-flow-in-the-NoC
RipTide v. SNAFU & ASICs

## Slide 101: Remaining
Progress made by this thesis
Future work
Conclusion
90%
Progress…

## Slide 102: This thesis v. COTS MCUs
90%
Progress…
Energy savings
Speedup

## Slide 103
Have we made enough progress?
90%

## Slide 104
Have we made enough progress?
90%

## Slide 105
Have we made enough progress?
90%

## Slide 106
Have we made enough progress?
90%

## Slide 107
Have we made enough progress?
90%

## Slide 108
Have we made enough progress?
90%
Other objectives can now be addressed

## Slide 109: Future work: Area efficiency
Possible solutions
Time-multiplexing
Alternative control-flow models
Higher-order primitives
Optimized topologies
RipTide
DMM
Sort
FFT
≈0.25mm2

## Slide 110: Future work: Performance
Parallelization
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
1cm2 chip fits ≈4000 6x6 RipTide fabrics
1.2TOPS @ ≈ 13W & 500MHz
Challenges
Data supply
Control
Speculation

## Slide 111: Future work: Performance
Parallelization
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
1cm2 chip fits ≈4000 6x6 RipTide fabrics
1.2TOPS @ ≈ 13W & 500MHz
Challenges
Data supply
Control
Speculation
Ld
St

## Slide 112: Future work: Performance
Parallelization
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
r
1cm2 chip fits ≈4000 6x6 RipTide fabrics
1.2TOPS @ ≈ 13W & 500MHz
Challenges
Data supply
Control
Speculation
Ld
St
Types
Memory, value, loop
Challenges
Misspeculation
Commit

## Slide 113: Future work: Compilation
Scaling mapping
Dataflow IR
Programming interface
Str
T
St
F
C
T
+
=
Str
Ld
Ld
x
*
*
Z
B
A
1
n
0
m
1
idx
idx
*
*
0
Splitting code
New solving methods

## Slide 114: Future work: Compilation
Scaling mapping
Dataflow IR
Programming interface
Str
T
St
F
C
T
+
=
Str
Ld
Ld
x
*
*
Z
B
A
1
n
0
m
1
idx
idx
*
*
0
F
C
T
+
Str
Ld
Ld
x
*
*
B
A
1
n
idx
*
*
Str
T
St
Z
0
m
1
idx
0
Call
Splitting code
New solving methods

## Slide 115: Future work: Compilation
Scaling mapping
Dataflow IR
Programming interface
"ID": 14,
"inputs": [
[{
"ID": 9,
"hold": false,
"name": "load_15",
"oport": 0,
"type": "data"
}],
[{
"ID": 8,
"hold": false,
"name": "load_13",
"oport": 0,
"type": "data"
}],
[{
"hold": true,
"type": "const",
"value": 5
}]
],
"name": "complx_30",
"op": "MUL_CFG_OP_CLIP",
"type": "MUL_FU_CFG_T"
O2P
Topology/microarchitecture agnostic
Information  Fast optimization

## Slide 116: Future work: Compilation
Scaling mapping
Dataflow IR
Programming interface
Exposes more information to compiler
Higher-level primitives  increase productivity
Functional (Parallel patterns) 1
f(
)
f(
)
f(
)
f(
)
f(
)
map
1Prabhakar et al. Generating Configurable Hardware from Parallel Patterns. ASPLOS 2016.
RipTide’s general-purpose support
T
C
>
+

## Slide 117: Summary
SONIC: Deploying DNNs on ULP devices
MANIC: ULP Vector-dataflow Co-processor
SNAFU & RipTide: ULP CGRAs
T
C
>
+
RipTide: Dataflow Compiler
Application
Compilation
OS
Architecture
Silicon
MANIC Silicon
New system stack:

## Slide 118: Acknowledgements
My advisors
Primary Collaborators
National Science
Foundation
Danny Bankman, Jaewon Shin
Brandon Lucia
Nathan Beckmann
Ken Mai
Oguz Aatli
Apple Scholars in AI/ML PhD Fellowship
Souradip Ghosh
Tony Nowatzki
Todd Mowry

## Slide 119: Summary
SONIC: Deploying DNNs on ULP devices
MANIC: ULP Vector-dataflow Co-processor
SNAFU & RipTide: ULP CGRAs
T
C
>
+
RipTide: Dataflow Compiler
Application
Compilation
OS
Architecture
Silicon
MANIC Silicon
New system stack:
Questions?

## Slide 120: Basic primitives
D
A
T
Steer
A
1
A
if(D) out = in
D
A
F
A
0
A
if(!D) out = in
T
C
>
+

## Slide 121: Basic primitives
D
A
T
Steer
if(D) out = A
D
A
F
if(!D) out = A
Carry: initblock
C
D
A
B
Init
Block
D, B;
Pop D, B
!D;
Pop D
A;
Pop A
State
machine
A
A
if(state == I) out = in
else if(D) out = in
T
C
>
+

## Slide 122: Basic primitives
D
A
T
Steer
if(D) out = A
D
A
F
if(!D) out = A
Carry: blockblock
C
D
A
B
Init
Block
D, B;
Pop D, B
!D;
Pop D
A;
Pop A
State
machine
D
B
if(state == I) out = A
else if(D) out = B
B
T
C
>
+

## Slide 123: Basic primitives
D
A
T
Steer
if(D) out = A
D
A
F
if(!D) out = A
Carry: blockinit
C
D
A
B
Init
Block
D, B;
Pop D, B
!D;
Pop D
A;
Pop A
State
machine
!D
if(state == I) out = A
else if(D) out = B
T
C
>
+

## Slide 124: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
0
0
a:
b:
z:
n = 2

## Slide 125: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
0
0
a:
b:
z:
n = 2
0
I
B

## Slide 126: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
0
0
a:
b:
z:
n = 2
I
B
0
0

## Slide 127: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
0
0
a:
b:
z:
n = 2
I
B
T
0
T

## Slide 128: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
0
0
a:
b:
z:
n = 2
I
B
0
0
0
0
T

## Slide 129: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
0
0
a:
b:
z:
n = 2
I
B
0
1
T

## Slide 130: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
0
0
a:
b:
z:
n = 2
I
B
1
1
0

## Slide 131: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
5
0
a:
b:
z:
n = 2
I
B
T
T
1

## Slide 132: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
5
0
a:
b:
z:
n = 2
I
B
1
T
1
1
1

## Slide 133: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
5
0
a:
b:
z:
n = 2
I
B
1
T
2

## Slide 134: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
5
0
a:
b:
z:
n = 2
I
B
2
2
1

## Slide 135: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
5
5
a:
b:
z:
n = 2
I
B
F
2
F

## Slide 136: Carry and steer in action
void vadd(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
z[i] = a[i] + b[i];
}
}
C
st
ld
ld
+
>
+
T
n
1
a
b
z
0
RipTide’s compiler
T
C
>
+
1
2
4
3
5
5
a:
b:
z:
n = 2
I
B

## Slide 137: RipTide supports nests
void test(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
...
for(int j = 0; j < n; j++) {
...
}
...
}
}
T
C
>
+
C
>
+
T
n
1
C
>
+
T
n
1
0
i
j

## Slide 138: RipTide supports nests
void test(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
...
for(int j = 0; j < n; j++) {
...
}
...
}
}
T
C
>
+
C
>
+
T
n
1
C
>
+
T
n
1
0
i
j
T
I
B
Blocks consumption until back in init state

## Slide 139
T
C
>
+
Dataflow compilation pipeline
void test(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}

## Slide 140: Dataflow compilation pipeline
T
C
>
+
void test(int *a, int *b, int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}
%i = Φ(0, %inc.i)
%cond.i = cmp lt, %i, %n
loop.i:
%j = Φ(0, %inc.j)
%cond.j = cmp lt, %j, %n
%a.j = load %a.i %j
%cond = cmp lt, %a.i, 0
store %z, %j, 0
%b.j = load b,%j
%z.j = load z,%j
%sum = add %b.j, z.j
store %z, %j, %sum
%inc.j = add %j, 1
%inc.i = add %i, 1
loop.j:
cond.j:
if:
body.j:
inc.i:
Control-flow graph
exit
LLVM

## Slide 141: Dataflow compilation pipeline
T
C
>
+
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
} }
}
LLVM
LSO
Store-store dependence
 Convert memory dependences to data dependences
loop.i
loop.j
cond.j
if
body.j
CFG
exit
inc.i

## Slide 142: Dataflow compilation pipeline
T
C
>
+
%i = Φ(0, %inc.i)
%cond.i = cmp lt, %i, %n
loop.i:
%j = Φ(0, %inc.j)
%cond.j = cmp lt, %j, %n
%a.j = load %a.i %j
%cond = cmp lt, %a.i, 0
%dep = Φ(0, %d)
%b.j = load b,%j
%z.j = cgra.ld z,%j,%dep
%sum = add %b.j, z.j
store %z, %j, %sum
%inc.j = add %j, 1
%inc.i = add %i, 1
loop.j:
cond.j:
if:
body.j:
inc.i:
exit
%d = cgra.st %z, %j, 0
CFG w/ Load-store ordering
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}
LLVM
Store-store dependence
 Convert memory dependences to data dependences
loop.i
loop.j
cond.j
if
body.j
CFG
exit
inc.i
LSO

## Slide 143: Dataflow compilation pipeline
T
C
>
+
LSO
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}
LLVM
loop.i
loop.j
cond.j
if
body.j
CFG
exit
inc.i
loop.i
loop.j
cond.j
if
body.j
CFG w/ LSO
exit
inc.i
Control-flow insertion
C
>
+
T
n
1
0
C
>
+
T
n
1
ld
ld
a
b
>
0
T
st
ld
z
z
0
+
st
z

## Slide 144: Dataflow compilation pipeline
T
C
>
+
LSO
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}
LLVM
loop.i
loop.j
cond.j
if
body.j
CFG
exit
inc.i
loop.i
loop.j
cond.j
if
body.j
CFG w/ LSO
exit
inc.i
CF
Insert
ld
ld
a
b
>
0
T
st
ld
z
z
0
+
st
z
Optimize
Str
Str
0
n
1
0
n
1
T
DFG

## Slide 145: Dataflow compilation pipeline
T
C
>
+
LSO
void test(int *a, int *b,
int *z, int n) {
for(int i = 0; i < n; i++) {
for(int j = 0; j < n; j++) {
if(a[j] < 0) {
z[j] = 0;
}
z[j] += b[j];
}
}
}
LLVM
loop.i
loop.j
cond.j
if
body.j
CFG
exit
inc.i
loop.i
loop.j
cond.j
if
body.j
CFG w/ LSO
exit
inc.i
CF
Insert
Optimize
DFG
Optimized
DFG